The FTS (Fast Track Service) - Sealing Layer is used for classification of the sealing densities of class 1.1 Urban fabric in level 3 and level 4.

| Legend Table URBAN ATLAS |
| --- |
| 1 | Artificial surfaces |
|  | 11 | Urban Fabric |
|  |  | 11100 | Continuous Urban Fabric (S.L.: > 80%) |
|  |  | 11210 | Discontinuous Dense Urban Fabric (S.L.: 50% - 80%) |
|  |  | 11220 | Discontinuous Medium Density Urban Fabric (S.L.: 30% - 50) |
|  |  | 11230 | Discontinuous Low Density Urban Fabric (S.L.: 10% - 30%) |
|  |  | 11240 | Discontinuous Very Low Density Urban Fabric (S.L. < 10%) |
|  |  | 11300 | Isolated Structures |
|  | 12 | Industrial, commercial, public, military and privates units |
|  |  | 12100 | Industrial, commercial, public, military and private unit |
|  |  | 12210 | Fast transit roads and associated land |
|  |  | 12220 | Other roads and associated land |
|  |  | 12230 | Railways and associated land |
|  |  | 12300 | Port areas |
|  |  | 12400 | Airports |
|  | 13 | Mine, dump and constructions sites |
|  |  | 13100 | Mineral extraction and dump sites |
|  |  | 13300 | Construction sites |
|  |  | 13400 | Land without current use |
|  | 14 | Artificial non-agricultural vegetated areas |
|  |  | 14100 | Green urban areas |
|  |  | 14200 | Sports and leisure facilities |
| 2 | Agricultural + Semi-natural + Wetlands areas |
| 3 | Forest (natural and plantation) |
| 5 | Water |

Soil Sealing layer was produced in 2008 based on Image 2006 data for 38 countries including the EU 27. The production of this initial 2006 GMES Fast Track Service Precursor (FTSP) on Land Monitoring, specifically the degree of soil sealing, was based on the derivation of a built-up mask, based on a hybrid ISODATA/Maximum Likelihood classification with manual corrections. The derivation of a sealing level within the built-up mask was based on NDVI derived from Image 2006 and visually interpreted calibration sites. This was used to derive a linear regression model of the degree of sealing ensuring that the highest NDVI value for unvegetated surfaces was set to 100 and the smallest NDVI value for an area fully covered by vegetation was set to 0. Therefore, the FTSP2006 degree of the sealing layer was based on vegetation activity within a land cover based built-up mask (i.e. an airport runway may be included, but not the grassland around it) excluding mines, quarries or construction sites that are unsealed and generally un-vegetated.